## Slide 1
Setup A, the starting point: nothing from the target camera
Trained on BRSET alone. This is the zero-shot transfer test, and it is the number every later experiment has to improve on.
BRSET train 11,372 tabletop images
mBRSET test 732 handheld images
ConvNeXt V2 Large trained on BRSET only same weights same cutoff
on BRSET, its own data 10 of 162 missed
on mBRSET, unseen camera 50 of 159 missed
Ranking barely suffers: AUC falls 0.9906 to 0.9060, so the model still separates diseased from healthy on phone images. The decision is what collapses, with recall dropping 0.938 to 0.686.
Two things change at the same time, which is what makes this hard
The camera degrades. 83 percent of mBRSET images carry an artifact.
The population changes. 6.6 percent with DR becomes 23.3 percent.
Setup A is the reference point, not the current design. The project has since moved to Setup B, which allows mBRSET images in training. That is on the next slide.

## Slide 2
Setup A and Setup B, kept separate
Training may draw on any available data. Only the 732-image mBRSET test split is protected, and it is identical across every experiment.
 | Setup A (zero-shot) | Setup B (aggregated training)
Training images | BRSET only, 11,372 | BRSET 11,372 + mBRSET 3,402 = 14,774
mBRSET labels used in training | No | Yes
Test images | mBRSET, 732 | mBRSET, 732 (identical images)
DR diseased-class F1 | 0.7842 | 0.8250
DR patients missed | 50 of 159 | 27 of 159
ME diseased-class F1 | 0.7027 | 0.8649
Experiment 0: the aggregated run, in full
Data | Configuration | Health and result
Train 14,774 (BRSET 77%, mBRSET 23%) Val 725 and test 732 are mBRSET ONLY DR positives 10.5% overall | ConvNeXt V2 Large, 512 px AdamW lr 3e-5, 25 epochs, 3 warmup focal gamma 2.0, no oversampling EMA 0.999, 4-way flip TTA, bf16 | 25 of 25 epochs, zero non-finite batches best epoch 10, 6.64 hours on one A40 DR AUC 0.9377, ME AUC 0.9936 ME precision 1.0000 (no false positives)
Honest reading: aggregation misses the fewest DR patients of any model and reaches perfect ME precision, but paired bootstrap puts it in a statistical tie with fine-tuning on DR (p = 0.47). It is a tie that catches more patients, not a win.

## Slide 3
Where the remaining gap lives
Diabetic retinopathy, diseased-class F1 on the mBRSET test set. Reading left to right, each step is a different kind of fix.
0.7842
Setup A, as transferred
0.7927
best possible cutoff
0.8355
best model trained with mBRSET labels
+0.009
+0.043
all a better cutoff can give
no cutoff reaches this. It needs a better model
At most 28 percent of the gap is the decision cutoff. At least 72 percent is the representation.
Endpoint used as the target | Its F1 | Share that is cutoff | Share that is representation
mBRSET from scratch, old recipe | 0.8146 | 28% | 72%
mBRSET from scratch, stable schedule | 0.8239 | 22% | 78%
BRSET and mBRSET trained jointly (Setup B) | 0.8250 | 21% | 79%
BRSET pretrain then mBRSET finetune | 0.8355 | 17% | 83%
The 0.7927 ceiling came from sweeping every cutoff from 0.005 to 0.995. Calibration, temperature scaling and label-shift correction only rescale scores, so none of them can pass it. That whole family is ruled out by measurement rather than by trial.

## Slide 4
The obstacle, and the proposed way around it
The camera-adaptation papers all assume paired data, the same patient on both devices. BRSET and mBRSET share no patients.
What the published methods need
Patient A on the tabletop camera
Patient A on the handheld camera
PAIRED
What this project actually has
BRSET 8,524 patients
mBRSET 1,291 different patients
NOT PAIRED
The proposed answer: device-fitted degradation
One BRSET image
the same image, degraded to match the handheld camera
PAIRED
Degradation augmentation manufactures the pairs that do not exist naturally
A clean image and its degraded twin are the same image, so they pair perfectly by construction. Creating them costs nothing.
The method: fit the degradation to the measured statistics of the real handheld camera, using the physically grounded fundus degradation model of Shen et al., cofe-Net, IEEE TMI 2021. That fitting is what makes the synthetic pairs realistic enough to learn from, and it is the novel step.
This matters beyond answering the objection. Every method that requires pairs was closed to this project and is now open, including clean-to-degraded feature distillation.

## Slide 5
The proposed method, and where each piece comes from
Four steps. Every step is published work; the contribution is the chain and the fitting in step 2.
1. Measure
How the handheld camera really degrades images, from 4,272 artifact-annotated mBRSET images
cofe-Net IEEE TMI 2021
2. Degrade
Apply that measured degradation to BRSET, creating clean and degraded pairs
GDRNet MICCAI 2023
3. Distil
Clean features teach the degraded ones, weighted by how hard each region is to recover
Self-Feature Distillation ECCV 2022
4. Separate
Split what both cameras share from what is specific to each, inside the encoder
Domain Separation Nets NeurIPS 2016
Steps 1 and 2 use no target diagnosis labels, only image appearance and existing artifact annotations.
What is genuinely new, and what would disprove it
Step 2 is the keystone. GDRNet fires its nine operations at a fixed 0.5 probability with hand-chosen magnitudes, tuned for no particular camera. Fitting them to a measured target device is the new part, and it is what makes the pairs realistic enough for step 3 to work.
The control: generic FundusAug at its published settings. If fitting to the device does not beat guessing, the contribution fails and I will report that. Gulrajani and Lopez-Paz, ICLR 2021, is the reason that control is not optional.
Deployable on a new camera without a labelling campaign, which is the practical case.

## Slide 6
Three findings from the widened review
The review was widened from the application to the semantics of the problem: two datasets with the same content, one high quality and one low.
A
The unpaired problem is solved in CT, not ophthalmology
DuDoNet (CVPR 2019) is dual-domain but needs PAIRED data. DCDiff (MICCAI 2024) extends it with conditional diffusion. The CycleGAN family escaped the paired requirement through cycle-consistency: translate low quality to high quality and then back again, recovering the original. The catch, worth a paragraph in the paper: CycleGAN is documented to collapse on real tabletop to portable fundus data (Lin, MICCAI 2022). Borrow the framing, not the method.
B
The routing idea has a name and a 2016 ancestor
Domain Separation Networks (NeurIPS 2016) is almost exactly what he sketched: a shared encoder for what both domains have in common, a private encoder per domain for what is specific, no paired data required. For the conditional-entropy half there is an active literature on information-theoretic gating for Mixture-of-Experts, where routing is driven by mutual information between expert assignment and label. Neither piece is ours; the combination on cross-device fundus appears open.
C
The generative world model idea is partly taken
A world model for cross-domain relationships looked unexplored. It is not. CheXWorld (CVPR 2025) is a self-supervised world model for radiographs that explicitly models domain variation across hospitals and devices. It validates the direction at a top venue, but the claim must be narrower: CheXWorld does self-supervised pretraining on chest X-ray, not cross-device transfer of a trained classifier.
Finding B is the one to act on: it gives the routing proposal a published architecture.

## Slide 7
The evidence behind each choice
Peer-reviewed venues only. Most sit outside ophthalmology, which is the point. Paper names are links.
Use | What it establishes | Paper | Venue
Adopt | Clean features can teach degraded ones, using synthetically degraded images. Exactly the setting here once step 2 makes pairs | Self-Feature Distillation | ECCV 2022
Adopt | Degradation and appearance augmentation beat every adaptation method tested for cross-scanner shift | Tellez et al. | Med. Image Anal. 2019
Adopt | Shared encoder plus a private encoder per domain, no pairs needed. The architecture behind the routing idea | Domain Separation Networks | NeurIPS 2016
Compare | Aligns low-quality features to high-quality ones through a fixed invertible decoder | QualNet | CVPR 2021
Frame | The same problem in CT: two views, one clean and one corrupted. Needs paired data, which is the limitation inherited here | DuDoNet | CVPR 2019
Bound | World model that already captures cross-device domain variation, so the novelty claim must be narrower | CheXWorld | CVPR 2025
Rule out | Adversarial adaptation collapses on real tabletop to portable data | Lin et al. | MICCAI 2022
Rule out | Test-time adaptation loses up to 66 points under prior shift | Boudiaf et al. (LAME) | CVPR 2022
Three of the four approaches worth trying first are published failures in this exact setting.

## Slide 8
Experiment 1: encoder separation, and what the adversarial term was doing
Four runs on the same aggregated training set. Only the architecture and the adversarial weight change. All 25 of 25 epochs, no instability.
Run | Adversarial weight | DR AUC | DR F1 | DR recall | DR missed | ME F1 | ME missed
Plain aggregated training (no separation) | not used | 0.9377 | 0.8250 | 0.8302 | 27 / 159 | 0.8649 | 15 / 63
Shared plus private encoders | 0.25 | 0.9448 | 0.8053 | 0.7673 | 37 / 159 | 0.8224 | 19 / 63
Shared plus private encoders | 0.05 | 0.9404 | 0.8227 | 0.7736 | 36 / 159 | 0.8889 | 11 / 63
Shared plus private encoders | 0.00 | 0.9441 | 0.8232 | 0.8050 | 31 / 159 | 0.8833 | 10 / 63
What the sweep shows
The adversarial term was the problem. Turning it down from 0.25 to 0.05 to zero raises DR F1 from 0.8053 to 0.8227 to 0.8232, and cuts missed patients from 37 to 31. It was scrubbing device information the decision still needed, which is why ranking improved while recall fell.
Even with it switched off, encoder separation does not beat plain aggregated training. On DR the two are indistinguishable (difference 0.0015, p = 0.91) and plain training still catches four more patients. On macular edema separation is ahead (10 missed against 15), but the difference is not significant (p = 0.50).
Sweeping every cutoff confirms it is not a threshold artifact: the best DR F1 reachable is 0.8361 for separation against 0.8383 for plain training. There is no hidden advantage waiting behind a better operating point.
A hypothesis that turned out to be wrong, recorded rather than dropped: the deficit was expected to come from selecting checkpoints on the average of AUC and F1. Reselecting on F1 alone chose the same epoch and gave identical numbers, so that explanation is ruled out.
Encoder separation alone is a wash. The routing gate now has to carry the contribution itself.

## Slide 9
What runs next
Every experiment reports against the same 732-image mBRSET test set.
 | Experiment | Outcome | Status
0 | Plain aggregated training | DR F1 0.8250, 27 of 159 missed. Still the model to beat | Done
1 | Shared plus private encoders, adversarial weight 0.25 | DR F1 0.8053, 37 missed. Worse than the baseline | Done
1a | Same, checkpoints selected on macro F1 alone | Identical result. The selection criterion was not the cause | Done
1b, 1c | Adversarial weight reduced to 0.05, then to zero | Recovers to DR F1 0.8232 and 31 missed, and to 10 of 63 on macular edema. Still a wash against the baseline | Done
2 | Entropy-gated routing, built on the weight-zero variant | The routing proposal itself. Both entropy formulations tested | Next
3 | Device-fitted degradation and distillation | Control is generic FundusAug at its published settings | Planned
What the negative result changes
Experiment 2 now builds on the weight-zero variant rather than the published defaults, because the sweep showed those defaults actively hurt on this problem.
The routing gate has to beat plain aggregated training on its own. It can no longer be presented as an addition to a structure that was already helping, because that structure is not helping.
Methodology settled through September, experiments through early October, target mid-October.